## Slide 1: What Happened to my Colours!?! Displaying console computer graphics on a TV
Bruce Dawson
Humongous Entertainment
bruced@humongous.com
http://www.cygnus-software.com/papers/

## Slide 2: Introduction
Computer graphics display badly on TVs
The reasons why are poorly understood
The main problems are:
  Interlaced flicker
  Illegal colours
  Limited resolution
Hi-res games can’t ignore the problems

## Slide 3: Yes, I spell colour with a ‘u’
I’m Canadian, eh?

## Slide 4: Purpose of this talk
Describe the problems in a clear and simple way
Explain why the problems exist
Give suggestions on how to deal with these problems

## Slide 5: Author background
Started writing computer games in 1987 for the Commodore Amiga, a ‘video synchronized’ computer
Worked for Elastic Reality/Avid on professional special effects and video editing software
Working on game for next-gen console at Humongous Entertainment

## Slide 6: Flickering images
Images which are rock solid on a computer monitor may flicker badly when displayed on a TV
This happens because each line is only scanned out thirty times per second
The “fusion frequency” is generally around 50-60 flashes per second (Hz)

## Slide 7: Interlace
Electron beam scans entire screen sixty (actually 59.94) times per second
Only draws every other line each time
Each pass is called a ‘field’
Two fields make a ‘frame’
This is known as an interlaced display
Demo...

## Slide 8: Why interlace?
Best use of limited broadcast bandwidth
Alternatives were:
  Use more bandwidth: fewer channels
  30 fps non-interlaced: worse flicker
  Use half as many lines: lower resolution
  Buffer each frame and show it twice: not possible in 1941
The alternatives were all worse

## Slide 9: Dealing with interlace
TV shows and movies don’t flicker much - we need to learn from them
Worst case is a thin white line on a black background. Don’t do this.
Avoid sudden transitions in general - soften them by blurring vertically
If ‘blurring’ sounds bad, call it “vertical filtering of out of bounds frequencies”

## Slide 10: Accepting reduced resolution
Reducing vertical resolution is annoying
However, keeping it is actually worse
You’re not giving up resolution - you never really had it.
‘Kell factor’ suggests maximum vertical resolution is 70% of line count

## Slide 11: Accepting reduced resolution
Going from 320x240 to 640x480 does not mean your vertical resolution has doubled
Professional video cameras and encoders all limit vertical detail
Console video encoders vary, but most have an option for vertical filtering

## Slide 12: Simulating resolution
You can simulate fine detail by using antialiasing
Dim lines will be perceived as thinner
Fonts should be antialiased, to allow finer detail with less blurring
This is most important on static screens – movement hides some flicker

## Slide 13: Real-time vertical filtering
Enable vertical filtering if it’s available
Requires vertically adjacent detail for best results - a full frame image
Rendering full frames at 60Hz is ideal
Rendering fields at 60Hz can work well, if the previous field is retained for filtering
Use a 16-bit frame buffer if necessary

## Slide 14: Illegal colours
Computers use the RGB colour space - all pixel colours are made by combining red, green, and blue
NTSC uses YUV or YIQ
Y stands for luminance - brightness
Y = .299R’ + .587G’ + .114B’

## Slide 15: YUV
If R, G, and B are all equal then Y will equal R, G, and B.
We can store colour information by recording how far B and R are from Y
U = 0.492(B’ - Y)
V = 0.877(R’ - Y)
Demo...

## Slide 16: YIQ
NTSC doesn’t use YUV, it uses YIQ
YIQ is a rotation of the U and V axes 33 degrees, so they line up with the way our brains process colour
I = V cos(33) - U sin(33)
Q = V sin(33) + U cos(33)

## Slide 17: Putting Y, I and Q together
First, I and Q are combined to make C, also known as chroma
C is a sine wave. Its amplitude represents saturation, and its phase represents hue
Y and C are combined through simple addition to make a composite signal

## Slide 18: Why does this matter?
For highly saturated colours C has a substantial amplitude
This means that Y+C has a much greater range than Y
Demo...

## Slide 19: More on illegal colors
It is physically impossible to broadcast some colours outside of this range
Illegal colours can interfere with sound
TVs are not designed to handle these colours, so they do it poorly
Highly saturated colours make interference between C (chroma) and Y more likely

## Slide 20: Fixing illegal colours
The worst illegal colours are red, blue, yellow, and cyan
Simplest fix is to reduce saturation
Reducing luminance works, but drastically changes the colour
It is easy to write code that detects and highlights or fixes illegal colours
Demo...

## Slide 21: Why YIQ?
YIQ was chosen for the NTSC standard because of the compatibility it provided - Y equaled the monochrome TV signal
It was also chosen because our eyes are most sensitive to detail in Y, less sensitive to detail in I, and least sensitive in Q
Demo...

## Slide 22: Frequency limits
I and Q can be stored and broadcast at lower resolution, without it being noticeable
Maximum bandwidth of Y is 4.2 MHz
Maximum bandwidth of I is 1.3 MHz
Maximum bandwidth of Q was 0.6 MHz, now it has been increased to 1.3 MHz

## Slide 23: Resolution limits
640x480x30 fps is 9,216,000 pixels per second
4.2 MHz signal is roughly equivalent to 8.4 million samples
25% of those are spent on horizontal and vertical blanking
Maximum NTSC horizontal resolution is at best 425, and 250-330 is more likely

## Slide 24: Comb filters
Colour and luminance information overlap in frequency space
Maximum horizontal resolution requires a comb filter in the TV
Comb filters assume adjacent lines have little colour variation
Colour changes can show up as Y detail

## Slide 25: Even lower resolution limits
Since I and Q are limited to 1.3 MHz, their effective resolution is even lower
This is less of a problem, since I and Q are a lot less important

## Slide 26: Follow the rules
If you put in horizontal detail beyond these limits then - without an S-Video or component connector - your customers cannot see it
If it makes it to the TV it will be as chroma crawl or other image defects
Good encoders will filter out the high frequencies, but you can help them

## Slide 27: Same solution as before
Deal with the horizontal resolution limits just like interlaced flicker
  Fonts and other fine detail should be antialiased
  Dimmer lines will be perceived as thinner
Television producers deal with this by avoiding fine stripes, herringbone patterns, checkers, etc.
Notes: Here are some notes

## Slide 28: Antialiasing matters - a lot
High frequencies cause many problems
Aliasing causes high frequencies
Blurry TVs don’t hide aliasing
Aliased edges are the biggest causes of chroma crawl and interlaced flicker
Distant textures that aren’t mip-mapped, or tiny polygons, cause aliasing that blurriness cannot possibly hide

## Slide 29: What about PAL?
PAL has a higher bandwidth signal - 60% more per field
There are no illegal colours in PAL
Interlaced flicker is worse, due to the 50 Hz refresh rate
Your animations need to handle 25/50 Hz updates as well as 30/60

## Slide 30: HDTV
HDTV is great
The lowest resolution is 720x480, it’s not interlaced, and all of those pixels are really there
Nobody has HDTV yet - maybe the new consoles will give people a reason to buy it

## Slide 31: CBS
NTSC was not the first North American colour TV standard - CBS invented a short lived standard
144 fields per second, cycling through red, green and blue
A colour wheel in the set spinning at 1440 RPM added colour

## Slide 32: It needn’t be this way
All of the limitations of NTSC only apply when you are transmitting signals
These limits needn’t apply when transmitting from inside the living room!
TV tubes can display arbitrary RGB
Composite video is only used because of lack of demand for better connectors

## Slide 33: Other considerations
When creating content, think about calibrating your monitors, and keep the lights on
Keep vital information inside the “text safe area”, to make sure it is visible on all TVs

## Slide 34: What can consumers do?
Don’t put many signals on one wire
  RF is worst
  Composite is also bad
  S-Video is great, and component is better
  Europeans should use a SCART connector

## Slide 35: What can developers do?
Test on cheap, old TVs with composite connectors, maybe even RF
Test on new TVs with comb filters
Check for illegal colours
Avoid excessive detail
Simulate fine detail with dim lines

## Slide 36: What else can developers do?
Antialias everything
Enable vertical filtering
Calibrate monitors
Turn the lights on
Respect the text safe area
Encoders may protect you, but they will be removing information

## Slide 37: For more information
Read the paper in the GDC proceedings
Consult the references listed in the paper
See Mike Nichols talk “From PC to TV”, also in the GDC 2001 proceedings
Look for more references, slides, new information, and sample programs at:
http://www.cygnus-software.com/papers/
Any questions?